## Slide 1
Enhancing ORB-SLAM2 with Monocular Cameras through Computed Depth Information
16-833 Robot Localization and Mapping
Zach Esakof, Connor Geshan, Jhanak Johri
Notes: Main title: 40 pt. Arial
Presenter Name: 16 pt. Arial
Presenters Title: 16 pt. Arial Italic

## Slide 2
Motivation
Background
Methodology
Results
Remaining Work

## Slide 3: We seek to improve the accuracy and efficiency of monocular ORB-SLAM2 by adding depth estimation for monocular images

## Slide 4: Monocular cameras are cheap and ubiquitous options in robotics
Notes: Monocular cameras are cheap and ubiquitous, but less efficient at depth estimation than cameras that use lasers (RGB-D) or multi-camera arrays (stereo).
Classical approaches require multiple monocular images before depth information is available.

## Slide 5: Depth estimation from a single image is a popular research topic in academia
D. Wofk et al.
Notes: Value in having depth information available immediately for a single image
  Triangulation from stereo won’t work and no laser readings are available for standard monocular camera
  Learning-based approaches to depth estimation
  Avoid sacrificing accuracy for speed
  One-shot depth estimation improves SLAM system initialization

## Slide 6
Motivation
Background
Methodology
Results
Future Works

## Slide 7: FastDepth is a lightweight, learning based, encoder-decoder network architecture.
RGB input, Depth Ground Truth and Estimated Depth Map using FastDepth on our system
Notes: Depth Estimation - FastDepth
A lightweight encoder-decoder network architecture
Network pruning to reduce computational complexity and latency
Real-time!

## Slide 8: FastDepth is a lightweight, learning based, encoder-decoder network architecture.
RGB input, Depth Ground Truth and Estimated Depth Map using FastDepth on our system
Notes: Depth Estimation - FastDepth
A lightweight encoder-decoder network architecture
Network pruning to reduce computational complexity and latency
Real-time!

## Slide 9: ORB-SLAM2 is a SLAM system for monocular, stereo and RGB-D inputs
Notes: Depth Estimation - FastDepth
A lightweight encoder-decoder network architecture
Network pruning to reduce computational complexity and latency
Real-time!

## Slide 10
Motivation
Background
Methodology
Results
Remaining Work

## Slide 11
RGB Images
RGB & Depth Images
Depth maps
FastDepth module
ORB-SLAM2 module
Depth map processing
Notes: This is an outline of out proposed pipeline.

## Slide 12
RGB Images
FastDepth module
Raw RGB Input Images
Notes: - Start with monocular images

## Slide 13
RGB Images
FastDepth module
Estimated Depth Map

## Slide 14
Estimated Depth maps
Depth map processing

## Slide 15
Estimated depth maps converted to 8-bit greyscale
Depth map processing
Notes: - Convert those depth maps into 16 bit greyscale images.

## Slide 16
8-bit greyscale converted to 16-bit pixel intensities
Depth map processing

## Slide 17
Depth Images
Depth map processing
Pixel intensity of 1 equates to 100 cm.

## Slide 18
RGB & Depth Images
ORB-SLAM2 module

## Slide 19
Motivation
Background
Methodology
Results
Remaining Work

## Slide 20
Monocular SLAM | RGB-D SLAM w/ FastDepth Estimation | Raw RGB-D SLAM
0.692081 | 0.3555921 | 0.039608
RMSE (m)

## Slide 21
Monocular SLAM | RGB-D SLAM w/ FastDepth Estimation | Raw RGB-D SLAM
0.692081 | 0.3555921 | 0.039608
RMSE (m)

## Slide 22
Monocular SLAM | RGB-D SLAM w/ FastDepth Estimation | Raw RGB-D SLAM
0.692081 | 0.3555921 | 0.039608
RMSE (m)

## Slide 23
Motivation
Background
Methodology
Results
Remaining Work

## Slide 24: Run our system in real-time using FastDepth inference during run time
Notes:   Dramatic lighting - how does the algorithm behave when presented with a bright scene punctuated by deep shadow?
  Indoor vs. outdoor - does landmark detection perform better or worse between these settings?
  Featureless surfaces - how does the algorithm behave when presented with large, nondescript surfaces such as blank walls?
  Intermittent black-outs - how does the algorithm recover from temporary loss of image data?

## Slide 25: Collect custom datasets of challenging setting to push our system to the limit
Notes:   Dramatic lighting - how does the algorithm behave when presented with a bright scene punctuated by deep shadow?
  Indoor vs. outdoor - does landmark detection perform better or worse between these settings?
  Featureless surfaces - how does the algorithm behave when presented with large, nondescript surfaces such as blank walls?
  Intermittent black-outs - how does the algorithm recover from temporary loss of image data?

## Slide 26: Collect custom datasets of challenging setting to push our system to the limit
  Dramatic lighting
Notes:   Dramatic lighting - how does the algorithm behave when presented with a bright scene punctuated by deep shadow?
  Indoor vs. outdoor - does landmark detection perform better or worse between these settings?
  Featureless surfaces - how does the algorithm behave when presented with large, nondescript surfaces such as blank walls?
  Intermittent black-outs - how does the algorithm recover from temporary loss of image data?

## Slide 27: Collect custom datasets of challenging setting to push our system to the limit
  Dramatic lighting
  Indoor vs. outdoor
Notes:   Dramatic lighting - how does the algorithm behave when presented with a bright scene punctuated by deep shadow?
  Indoor vs. outdoor - does landmark detection perform better or worse between these settings?
  Featureless surfaces - how does the algorithm behave when presented with large, nondescript surfaces such as blank walls?
  Intermittent black-outs - how does the algorithm recover from temporary loss of image data?

## Slide 28: Collect custom datasets of challenging setting to push our system to the limit
  Dramatic lighting
  Indoor vs. outdoor
  Featureless surfaces
Notes:   Dramatic lighting - how does the algorithm behave when presented with a bright scene punctuated by deep shadow?
  Indoor vs. outdoor - does landmark detection perform better or worse between these settings?
  Featureless surfaces - how does the algorithm behave when presented with large, nondescript surfaces such as blank walls?
  Intermittent black-outs - how does the algorithm recover from temporary loss of image data?

## Slide 29: Collect custom datasets of challenging settings to push our system to the limit
  Dramatic lighting
  Indoor vs. outdoor
  Featureless surfaces
  Intermittent black-outs
Notes:   Dramatic lighting - how does the algorithm behave when presented with a bright scene punctuated by deep shadow?
  Indoor vs. outdoor - does landmark detection perform better or worse between these settings?
  Featureless surfaces - how does the algorithm behave when presented with large, nondescript surfaces such as blank walls?
  Intermittent black-outs - how does the algorithm recover from temporary loss of image data?